## Slide 1: Electrical Circuits
Properties of an electrical circuit include
Voltage Volts V
Current Amps A
Resistance Ohms Ω

## Slide 2: Kirchhoff’s Laws
Kirchhoff’s Voltage Law (KVL):
  The sum of all voltage drops in a series circuit equals the total applied voltage
Kirchhoff’s Current Law (KCL):
  The total current in a parallel circuit equals the sum of the individual branch currents
Ohm’s Law
V = IR
Electrical Power
P = V I
P = I
2
R
Circuit Equations - Summary
V = electrical potential (volts)
I = current (amps)
R = resistance (ohms)
P = power (watts)

## Slide 3: Current
The flow of electric charge
When the faucet (switch) is off, is there any flow (current)?
NO
When the faucet (switch) is on, is there any flow (current)?
YES
Tank (Battery)
Faucet (Switch)
Pipe (Wiring)
- measured in AMPERES (A)

## Slide 4: Current in a Circuit
When the switch is off, there is no current.
When the switch is on, there is current.
off
on

## Slide 5: Voltage
The pressure that causes current to flow
When the faucet (switch) is off, is there any pressure (voltage)?
YES – Pressure (voltage) is pushing against the pipe, tank, and the faucet.
When the faucet (switch) is on, is there any pressure (voltage)?
YES – Pressure (voltage) pushes flow (current) through the system.
Tank (Battery)
Faucet (Switch)
Pipe (Wiring)
- measured in VOLTS (V)

## Slide 6: Voltage in a Circuit
The battery provides voltage that will push current through the bulb when the switch is on.
off
on
off
on

## Slide 7: Resistance
The opposition of current flow
What happens to the flow (current) if a rock gets lodged in the pipe?
Flow (current) decreases.
Tank (Battery)
Faucet (Switch)
Pipe (Wiring)
- measured in Ohms (Ω)
Notes: All materials have resistance. Conductors have little resistance. Insulators provide a lot of resistance. Some electronic components (resistors) have a specific resistance. These are often needed to reduce current in order to protect other components or to adjust the amount of current that goes to other components.

## Slide 8: Resistance in a Circuit
Resistors are components that create resistance.
Reducing current causes the bulb to become more dim.
off
on
Resistor

## Slide 9: Ohm’s Law
Quantities | Abbreviations | Units | Symbols
Voltage | V | Volts | V
Current | I | Amperes | A
Resistance | R | Ohms | Ω
If you know 2 of the 3 quantities, you can solve for the third.
V=IR
The mathematical relationship between current, voltage, and resistance
Current in a resistor varies in direct proportion to the voltage applied to it and is inversely proportional to the resistor’s value

## Slide 10: Example: Ohm’s Law
  The flashlight shown uses a 6 volt battery and has a bulb with a resistance of 150 . When the flashlight is on, how much current will be drawn from the battery?
VT =
VR
IR
Schematic Diagram
V
I
R

## Slide 11: Circuit Configuration
Series Circuits
Components are connected end-to-end.
There is only a single path for current to flow.
Parallel Circuits
Both ends of the components are connected together.
There are multiple paths for current to flow.
Components
(i.e., resistors, batteries, capacitors, etc.)
Notes: Overview of series and parallel component configuration.

## Slide 12: Kirchhoff’s Laws
Kirchhoff’s Voltage Law (KVL):
  The sum of all voltage drops in a series circuit equals the total applied voltage
Kirchhoff’s Current Law (KCL):
  The total current in a parallel circuit equals the sum of the individual branch currents

## Slide 13: Series Circuits
A circuit that contains only one path for current flow
If the path is open anywhere in the circuit, current stops flowing to all components.

## Slide 14: Series Circuits
Use Ohm’s and Kirchhoff’s laws to analyze this circuit.
What is the total Resistance (ohms)?
What is the total Current (amps)?
What is the Voltage Drop (volts) across each resistor?
VT
+
-
VR2
VR1
VR3
IT
Notes: Characteristics of a series circuit.

## Slide 15: Example: Series Circuit
Solution:
V
I
R
Total Resistance:
Current Through Each Component:
Notes: This slide provides the solution. If you print handouts, do not print this page. (1 of 3)

## Slide 16: Example: Series Circuit
Voltage Across Each Component:
V
I
R
Solution:
Notes: This slide provides the solution. If you print handouts, do not print this page. (2 of 3)

## Slide 17: Parallel Circuits
A circuit that contains more than one path for current flow
If a component is removed, then it is possible for the current to take another path to reach other components.

## Slide 18: Parallel Circuits
Characteristics of a Parallel Circuit
The voltage across every parallel component is equal.
The total resistance (RT) is equal to the reciprocal of the sum of the reciprocal:
The sum of all of the currents in each branch (IR1 + IR2 + IR3) is equal to the total current (IT). This is called Kirchhoff’s Current Law.
+
-
+
-
VR1
+
-
VR2
VR3
RT
VT
IT
+
-
Notes: Characteristics of a parallel circuit.

## Slide 19
  For the parallel circuit shown, use the laws of circuit theory to calculate the following:
    The total resistance (RT)
    The voltage across each component (VT, V1, V2, & V3)
    The current flowing through each component (IT, I1, I2, & I3)
    Use the results to verify Kirchhoff’s Current Law
19
+
-
+
-
VR1
+
-
VR2
VR3
RT
VT
IT
+
-
IR1
IR2
IR3
Example Parallel Circuits
Notes: Pause the presentation and allow the student to work on the example. The solution is on the next three slides.

## Slide 20
Total Resistance:
Voltage Across Each Component:
Solution:
Example Parallel Circuits
Notes: This slide provides the solution. If you print handouts, do not print this page. (1 of 3)

## Slide 21
V
I
R
Current Through Each Component:
Solution:
Example Parallel Circuits
Notes: This slide provides the solution. If you print handouts, do not print this page. (2 of 3)

## Slide 22
Verify Kirchhoff’s Current Law:
Solution:
Example Parallel Circuits
Notes: This slide provides the solution. If you print handouts, do not print this page. (3 of 3)

## Slide 23: Combination Circuits
Contain both series and parallel arrangements
What would happen if you removed light 1? Light 2? Light 3?
1
2
3

## Slide 24: Electrical Power
Electrical power is directly related to the amount of current and voltage within a system.
Power is measured in watts
P = V I
P = I
2
R

## Slide 25: Kirchhoff’s Laws
Kirchhoff’s Voltage Law (KVL):
  The sum of all voltage drops in a series circuit equals the total applied voltage
Kirchhoff’s Current Law (KCL):
  The total current in a parallel circuit equals the sum of the individual branch currents
Ohm’s Law
V = IR
Electrical Power
P = V I
P = I
2
R
Circuit Equations - Summary
V = electrical potential (volts)
I = current (amps)
R = resistance (ohms)
P = power (watts)