Fluid Power Problems

Name and date submitted:

Directions

Answer the following questions. Sketch each, then label all known values. Be sure to include all steps and units throughout each solution.

All problems assume that conditions are ideal. Forces such as friction are not considered.

Problems

A pneumatic system is producing 100 lb/in.2 of gauge pressure. A cylinder is needed to press an adhesive label onto a product. It has been determined that 5 lb of force is optimal to complete this task. Use Pascal’s law: Pi = Po, or Fi/Ai = Fo/Ao

Sketch and label all known and unknown values.

Sketch

What is the required area of the pneumatic cylinder?

| Formula | Substitute / Solve | Final Answer |
| --- | --- | --- |

What is the required diameter of the pneumatic cylinder?

| Formula | Substitute / Solve | Final Answer |
| --- | --- | --- |

A hydraulic lift system utilizes two 3 in. diameter cylinders. Workers must determine how much the system is capable of lifting before deciding how much weight can be lifted safely. The system runs at a gauge pressure of 2000 lb/in.2.  Use the pressure formula, P = F/A.

Sketch and label all known and unknown values.

Sketch

What is the area of each piston?

| Formula | Substitute / Solve | Final Answer |
| --- | --- | --- |

How much is the system capable of lifting?

| Formula | Substitute / Solve | Final Answer |
| --- | --- | --- |

The gauge pressure of a pneumatic cylinder reads 20 lb/in.2 when the volume is 30 in.3. The cylinder is compressed until the gauge reads 60 lb/in.2.  Assume standard atmospheric pressure (14.7 psi). Use Boyle’s law: P1V1 = P2V2

Sketch and label all known and unknown values.

Sketch

What is the absolute pressure, Pabs, before and after the cylinder gas is compressed?

| Formula | Substitute / Solve | Final Answer |
| --- | --- | --- |

| Formula | Substitute / Solve | Final Answer |
| --- | --- | --- |

What is the volume in the cylinder after the gas is compressed?

| Formula | Substitute / Solve | Final Answer |
| --- | --- | --- |

The air temperature in a 28 in.3 container with a free sliding piston is initially measured at 45 °F. The temperature is raised to 200 °F.  What is the new volume of the container? Use Charles’ law: V1/T1 = V2/T2

Sketch and label all known and unknown values.

Sketch

What are the absolute temperature readings in degrees Kelvin, initially and after the temperature has been raised? ⁰K = 5/9 x (⁰F + 460)

| Formula | Substitute / Solve | Final Answer |
| --- | --- | --- |

| Formula | Substitute / Solve | Final Answer |
| --- | --- | --- |

What is the volume in the cylinder after the temperature has been raised?

| Formula | Substitute / Solve | Final Answer |
| --- | --- | --- |

A 60 ft3 compressor tank container has a gauge pressure of 160 lb/in.2 and a temperature of 70 °F. The temperature after some time decreases to 40 °F.   Find the final pressure in the tank.  Assume standard atmospheric pressure. Use Guy-Lussac’s law: P1/T1 = P2/T2

Sketch and label all known and unknown values.

Sketch

What are the absolute temperature readings in degrees Kelvin initially and after the temperature decreases?  ⁰K = 5/9 x (⁰F + 460)

| Formula | Substitute / Solve | Final Answer |
| --- | --- | --- |

| Formula | Substitute / Solve | Final Answer |
| --- | --- | --- |

What is the absolute pressure, Pabs, of the system before the temperature decreases?

| Formula | Substitute / Solve | Final Answer |
| --- | --- | --- |

What is the absolute pressure, Pabs, of the system after the temperature decreases?

| Formula | Substitute / Solve | Final Answer |
| --- | --- | --- |

A flow meter is attached in a hydraulic line that measures 12 gal/min. The line has an inside diameter of 1.5 in.  Find the flow velocity in in./min. where the fluid passes the meter. Use the flow velocity equation: v = Q/A. 1 gal. = 231 in3.

Sketch and label all known and unknown values.

Sketch

What is the flow rate measured as in.3 /min at the meter?

| Formula | Substitute / Solve | Final Answer |
| --- | --- | --- |

What is the area of inside diameter of the line?

| Formula | Substitute / Solve | Final Answer |
| --- | --- | --- |

What is the flow velocity where the fluid passes the meter?

| Formula | Substitute / Solve | Final Answer |
| --- | --- | --- |

A hydraulic press must be used to press-fit two components together in an assembly process. The system must generate at least 775 lbs of force to perform the press fit. The piston at the input cylinder is pushed with a force of 250 lbs and has an area of 30 in.2.  The output can use up to 15 cylinders that are each 30 in.2.  How many cylinders are needed?

Sketch and label all known and unknown values.

Sketch

How much mechanical advantage is required to gain the necessary force?  MA = Fo/Fi

| Formula | Substitute / Solve | Final Answer |
| --- | --- | --- |

How many output cylinders must be incorporated into the design?